## Slide 1: Beyond Back of the Envelope
Yet-Ming Chiang
Ryan Boas

## Slide 2
Out of the comfort zone
Research
Business

## Slide 3: Attacking the Right Problem

## Slide 4: “Thinning the herd”- Dec. 3, 2008
Note: Public domain image. USDA 5/19/2003
240+ thin film PV companies
One clear success

## Slide 5: Live and Die By Your Cost Model
Be fluent in the concepts and mechanics of cost modeling
Use cost modeling to avoid the 4 most common pitfalls of technology development
Build your own cost model

## Slide 6: Basic concepts

## Slide 7: Price – COGS = Gross Margin
Chart: 
Price | 100
Material | 30
Depreciation | 15
Labor | 3
Other | 2
Gross Margin | 50
COGS
Definitions
Price – What the market pays
COGS – Cost of Goods Sold
  Materials
  + Depreciation
  + Labor
  + Other
BOM – Bill of Materials
Note: Materials ≠ BOM

## Slide 8: Depreciation = amortized CapEx
$250M
$25M
$1
Factory &
Equipment
(CapEx)
Yearly
Depreciation
Per-unit
Depreciation
10 yr Term
25M units

## Slide 9: Integrate Cost & Performance Models
 | Material A | Material B
COGS ($) | $750 | $1,000
Energy (kWh) | 2 | 2
Life (cycles) | 3,000 | 10,000
Life cycle cost ($/kWh) | $0.13 | $0.05
Cost Model
Integration
Performance Model

## Slide 10: Top Pitfalls

## Slide 11: The 4 most common pitfalls of developing technology without a guiding model
Attacking the wrong problem
Misunderstanding state of art and trajectory
Idealizing system costs and manufacturing
Blind to system sensitivities
© Andrew Dunn, 24 September 2005.

## Slide 12: Attacking the Wrong Problem
Source: Argonne BatPaC, v1.0. Battery 1 selected with default values.
Focus here.
Not here.

## Slide 13: Misunderstanding Trajectory
Chart: $ (thousands)
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Price | 100 | 90 | 80 | 70 | 60 | 50
Cost | 70 | 65 | 60 | 55 | 50 | 45

## Slide 14: Your Position in Trajectory
Chart: $ (thousands)
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Price | 100 | 90 | 80 | 70 | 60 | 50
Cost | 70 | 65 | 60 | 55 | 50 | 45
Your Cost | 130 | 110 | 90 | 70 | 50 | 30
You fund these losses.

## Slide 15: Idealizing: The 100% Fallacy
The long slog
The initial comparison
Where you start

## Slide 16: Misunderstanding Sensitivities
Tornado Chart Example for PEM Fuel Cells from: http://www1.eere.energy.gov/hydrogenandfuelcells/pdfs/mass_production_cost_estimation_report.pdf
HIGH Priority
LOW Priority

## Slide 17: How to get started

## Slide 18: Zeroeth Order – Back of the Envelope
A very simple back of envelope estimate is a great starting point.
Use raw materials costs to provide a rough lower bound on cost
Make optimistic guess of performance using modeling or lab results
Adjust roughly to accommodate balance of systems, yield, margins
Compare with state of the art (via experts, validated models)
Ask outside experts to give you their back-of-the-envelope assessment. Their intuition is highly valuable.

## Slide 19: Zeroeth Order – Things you can Google
Google is a great starting point, but don’t rely solely on reports, which can be erroneous or outdated – validate with experts in the field!
Source: BCG

## Slide 20: First Order – Develop a base model
A simple, but comprehensive model will be the workhorse for your technology development decisions.
Model the physical parameters of your system
  Model performance based on changes to those parameters
Tie design parameters to materials and component costs
  Use real cost data from reports or direct supplier research
  Take care on volume assumptions
Build a best-effort manufacturing model
Apply industry-standard adjustment factors for balance of systems, yield, and margins
Run a sensitivity analysis to see how design variables affect your key performance metrics
  Make sure you know which performance metrics are valued by the market

## Slide 21: Cost/Performance Model

## Slide 22: Argonne Battery Model Baseline
http://www.cse.anl.gov/batpac/index.html

## Slide 23: Behind the Charts - Materials

## Slide 24: Behind the Charts – Manufacturing

## Slide 25: Behind the Charts - Performance

## Slide 26: Capex Pareto
Source: Argonne BatPaC, v1.0. Battery 1 selected with default values.

## Slide 27: Sensitivity Analysis
D. M. Powell, M. T. Winkler, H. J. Choi, C. B. Simmons, D. B. Needleman and T. Buonassisi, Energy & Environmental Science, DOI:10.1039/C2EE03489A, 2012.

## Slide 28: Nth Order – Iterate and Expand
As the need arises, expand your model to include more complexity and detail
Use your model to drive design of experiments and refine the model based on results
Incorporate actual cost data for various projected volumes from specific potential suppliers
Develop internal models for balance of systems, yield, and margins based on actual design, manufacturing, and go-to-market plans.
Expand sensitivity analysis to help evaluate complex design trade-offs
Consider building a robust interface to allow for protected sharing of your model with potential investors, partners, etc.

## Slide 29: Know Thy Lingo
BOM (pronounced ‘bom’) vs. COGS
  BOM is the bill of materials, applies to a single unit
  COGS includes materials, depreciation, labor, other costs and is impacted by yield, utilization
Price vs. cost vs. margin
  Price set by market
  Cost (COGS) is the full cost to manufacture your product
  Margin is what is left to run the rest of the company and make a profit
Yield
  (Product that rolls off the mfg line minus damaged product) divided by (product that rolls off the mfg line)
Utilization
  The fraction of total factory capacity that was actually used. Total factory output divided by total factory capacity.
Tornado chart
  Chart that ranks the relative importance of cost inputs. Tells you what to focus on. Looks like a tornado (kind of).
Pareto chart
  Chart that shows individual contributions to cost in a ranked order.

## Slide 30: Summary
Quantify industry price and cost trends
Model COGS for your technology
  Start early
  Develop iteratively with best available information
Be realistic about the progression from today to your future vision

## Slide 31: Thank You.
24M Technologies, Inc.
One Kendall Square, Suite B6103
Cambridge, MA 02139
T: (617) 553-1012
F: (617) 553-1018
E: info@24-m.com