## Slide 1
Halotechnics High Throughput Chemistry and Materials Characterization
December 2015
Justin Raade, PhD
CEO and Founder
jraade@halotechnics.com
(510) 693-7116

## Slide 2: High throughput chemistry lab
Powerful product development lab built with $5 million in investment and federal R&D grants from NSF, DOE, and ARPA-E
Capable of developing molten salt, glass, and oxide products for a broad range of applications
Synthesize and screen 200 materials/day
High temperature materials are the key to abundant clean energy
Selected Partners and Customers
Seeking strategic acquirer interested in rapid product development of thermal materials

## Slide 3: Halotechnics Thermal Materials Applications
Halotechnics Thermal Materials Platform
Energy
Waste Heat Recovery
Power Generation
Glass manufacturing
Heavy oil upgrading
Energy storage for peak demand
Steel manufacturing
Thermal barrier coatings
In-situ oil shale conversion
Aluminum
smelting

## Slide 4: Laboratory Capabilities Summary
Laboratory Overview
Halotechnics has developed a complete suite of capabilities for thermal materials synthesis and characterization:
Proprietary material design software and database
High-throughput screening
Melting point, heat capacity, heat of fusion
Thermal stability
Viscosity
Density
Corrosion and materials compatibility

## Slide 5: 1. Material design software and database
PO4 0.950
PO4 0.650
PO4 0.350
PO4 0.050
Halotechnics custom-built software allows the designer to vary multiple salt ions and view the projected phase space in real time.
Once a design is settled, the candidates are dispensed, synthesized, and screened for melting point.
Searchable database of 23,000 mixtures including nitrates, chlorides, carbonates, sulfates, oxides

## Slide 6: 1. Material design software and database
Saltstream and Haloglass
Enabling a new class of applications in extreme heat
www.halotechnics.com/products
Halotechnics products were developed by screening over 23,000 unique mixtures
Properties in searchable database: composition, melting point, thermal stability

## Slide 7: 2. High-Throughput Screening
Workflow:
Halotechnics leverages its high-throughput chemistry screening capabilities
to survey thousands of multi-component materials across broad phase spaces.
Library Design
Powder Dispense
Parallel Melting Point Analysis

## Slide 8: 2. High-Throughput Screening
200
3000
20
5
Optimized molten salt
Melting
point
Heat
capacity
Viscosity
Corrosion
PMP
DSC
Viscometer
High throughput workflow capable of screening 200 mixtures/day

## Slide 9: 3. Melting point, heat capacity, heat of fusion
Differential Scanning Calorimeter (DSC): Netzsch 404 F1 Pegasus, 20-position autosampler
Measure thermal properties up to 1500 °C
  Melting point
  Heat of fusion
  Heat capacity
  Glass transition and crystallization
DSC graph of potassium nitrate

## Slide 10: 4. Thermal Stability
Thermogravimetric Analysis (TGA): TA Instruments Q500
Measure dehydration and decomposition reactions at temperatures up to 1000 °C
Atmospheric gas control, air vs inert
TGA thermal stability behavior of calcium oxalate reference material

## Slide 11: 5. Viscosity
Measure viscosity vs. temperature, a critical parameter for systems design/engineering.
Viscosity data for quaternary salt mixtures (Bradshaw and Siegel, 2009)
Modified Brookfield viscometer capable of measuring molten salt viscosity from room temperature up to 565 °C.
Orton molten glass viscometer capable of operation up to 1600 °C

## Slide 12: 6. Density
Measure density vs. temperature with Halotechnics’ custom-built Archimedean furnace density measurement system:
Stainless steel sinker hung beneath analytical balance
Sinker suspended in molten salt inside temperature-controlled crucible furnace
Buoyancy force offsets weight
Data acquisition system computes density as a function of temperature
Balance
Sinker
Molten salt
Crucible
Heating element

## Slide 13: 7. Corrosion and Materials Compatibility
Corrosion Testing Protocol
Crucible furnaces with stainless steel, carbon steel, and nickel-based coupons immersed in molten salt for 3000-hour corrosion test at temperatures up to 700 °C:
  Sample coupons at regular
  500-hour intervals
Post test analysis:
  Cross section analysis
  Weight loss
  Microscopy imaging
  Ion analysis of salt

## Slide 14: Salt development case study #1
Screened over 5,000 unique compositions in search of molten salt heat transfer fluid
Experiments surveyed a broad phase space of nitrate, nitrite, chloride, carbonate, and sulfate salts
Phase space with eutectic mixture of LiNO3-NaNO3-KNO3-CsNO3-Ca(NO3)2
J. W. Raade and D. Padowitz, Journal of Solar Energy Engineering, Vol. 133, Issue 3, 2011.

## Slide 15: Salt development case study #2
SaltstreamTM 700: High temperature heat transfer fluid consisting of ZnCl2-NaCl-KCl and related mixtures
PCT patent application filed, active status. IP available for acquisition.
Phase space with mixtures of ZnCl2-NaCl-KCl
J. W. Raade, J. Vaughn, B. Elkin, “Thermal energy storage with molten salt,” U.S. patent application 61/592,859, 2012.

## Slide 16: Glass development case study
High throughput glass chemistry screening
Graphite piping from molten glass test loop after testing at 1100 °C
Proprietary vanadium-based glass
Proprietary phosphate-based glass
(a)
(b)
(d)
(c)

## Slide 17: Glass development case study
Screened 397 unique glass compositions in search of thermal storage fluid
Experiments surveyed a broad phase space of silicate, phosphate, vanadate, and lead oxide glasses
B. Elkin, et al., Energy Procedia: Proceedings of SolarPACES, Volume 49, 2014.
100 distinct compositions are explored in a four-component phase space.